## Slide 1: EDES 301 NeuroSwitch: EEG Light Switch Proposal
2026.10.04
Sunny Yu

## Slide 2: Background Information
What is being proposed?
  A battery-powered brain-computer interface (BCI) built on the PocketBeagle
  Records one channel of EEG from the back of the head (occipital) and detects alpha waves (8–12 Hz) in real time
  Alpha power rises sharply when the eyes close: when the processed alpha power crosses above a threshold (eyes closed) the light turns off, and when it drops back below (eyes open) the light turns back on, with no hands needed
What is your story?
  My interest in neuroengineering motivates me to turn brain signals into useful actions. For my first EEG project, I want to build a complete acquire–process–act loop on a small, low-cost embedded Linux board. The goal is a standalone, hands-free switch that could help people with limited mobility control devices more independently.

## Slide 3: Background Information
Existing projects / libraries
  Upside Down Labs BioAmp EXG Pill: open-source biopotential front-end with EEG filter and eyeblink detection
  Typical alpha-wave “eyes-closed” demos (OpenBCI, BioAmp examples) process data on a PC
Improvements / additions over existing projects
  Software: all processing on the PocketBeagle in Python, with no PC: band-pass filter sliding-window alpha power if possible calibration based on user threshold-crossing detection that switches the light on / off
  Hardware: integrates the EEG front-end (scaled to the 1.8 V ADC range), an LED, a buzzer and a button into one battery-powered device that autoboots
  Evaluation: reports how often the light state matches the eye state, false-switch rate and switching latency
  Stretch goals (if time permits): blink-artifact rejection, logging EEG data to the SD card

## Slide 4: System Block Diagram
Gel electrodes
BioAmp EXG Pill
Resistor divider (÷2)
10 kΩ / 10 kΩ
Push button (pull-up)
mode: Calibrate / Run
Analog (µV)
0–3.3 V
PocketBeagle
0–1.65 V
Analog Input / AIN0 (ADC)
GPIO (interrupt)
LED lamp
3 large kit LEDs + 330 Ω
Buzzer (kit)
GPIO ×3
PWM
Light off (eyes closed)
on (eyes open)
Audio cues
calibration, mode changes
light
sound
Software loop: ADC (250 Hz) → band-pass 8–12 Hz → 1 s alpha power → threshold crossing → lamp off (eyes closed) / on (eyes open)

## Slide 5: Power Block Diagram
USB power bank
5 V, ≥1 A
PocketBeagle
~5 V in, 250–400 mA
3.3 V rail
GPIO / PWM pins (3.3 V)
VDD_ADC (1.8 V)
BioAmp EXG Pill
3.3 V, ~2 mA
Push button pull-up
3.3 V, <1 mA
LED
Buzzer (kit)
PWM, low current
ADC input (AIN0)
EEG ÷2 → ≤1.65 V
1.8 V max
Battery power only while electrodes are attached; no connection to wall power for user safety. All grounds common.

## Slide 6: Components / Budget
Component | EDES301 to Buy? | Cost
BioAmp EXG Pill kit (2 boards, 15 gel electrodes, cables) | Yes (partial) | $69.00
PocketBeagle (provided) | No | —
Large LEDs ×3 + 330 Ω resistors (parts kit) | No | —
Buzzer (parts kit) | No | —
Push button (parts kit) | No | —
Jumper wires + breadboard (parts kit) | No | —
USB power bank, 5 V (own) | No | —
Requested from EDES301: $35.00 (remaining ~$34 self-funded)
The BioAmp kit (Mouser) is the only part not on the EDES301 parts list.